## Slide 1: BINDT Aerospace Workshop - April 8th 2019 Materials for the Future Fighter and the challenges this brings for NDT Kevin Pickup – Lead Technologist – Product Verification BAE Systems Air

## Slide 2: INTRODUCTION Aircraft Through the Ages
Over the last century aircraft have changed significantly, in both the materials we use to make them and the way we use the materials in the structure, but WHY?
  Improved Strength - increased flight envelope and capability (more manoeuvrable)
    Improved life cycle (fatigue)
      Survivability & reparability from Battle damage
        Weight saving – performance enabler
          Optimised Aircraft Dynamics (aero elasticity & morphing structure)
            Available materials has improved
Early Wooden Fighter
Tornado ADV
Concept Future Fighter

## Slide 3: INTRODUCTION DRIVERS FOR CHANGE
ADAPTABLE
Lead Time to Market
Low Observability
QUALIFICATION TIME SPAN
AFFORDABLE
FLEXIBLE
Re-configurable
Environment& Efficiency

## Slide 4: CURRENT AIRCRAFT Materials Make Up
Bae Hawk
100% Metallic
Eurofighter Typhoon
Composite Skins
Metallic Frames
Future Fighter
? ? ?

## Slide 5: CURRENT AIRCRAFT ASSEMBLY PROGRESSION
Conventional Welding
Rivets - thousands of them!
Bonded Composites
Novel Fasteners
EB Welds
Diffusion Bonding
Co-Bonded Assemblies
????

## Slide 6: FUTURE FIGHTER DETAIL & ASSEMBLY MANUFACTURE
3D Composites
Z stitching
WAAM
Powder HIP
Friction Stir Welding
Linear & Spot
Paste Adhesive Bonded Primary Structure
Fibre Reinforced FDM/Plastics
Hybrid & Dissimilar Composites Materials
Thermoplastics
Metal Matrix Composites
Friction Stir Welding
RTM & LRI
AFP Toe Steering

## Slide 7: FUTURE MATERIALS 3D COMPOSITES – Raw Material form
The more complex the preforms become (tailored strength), the more critical to the structure.
  Therefore verification of the weave pattern may be required prior to consumption
  XCT required to define fibre orientation and path
  Large parts and undesired aspect ratio may hinder required resolution in XCT

## Slide 8: FUTURE MATERIALS THERMOPLASTICS
Thermoplastics have greater Durability and offer greater repair options and different joining options such as:
  Welding – both butt/splice joints and lap joints
  Tufting – mechanical and Z-Stitching
  Microwave curing
They also offer greater forming options:
  Hot Press forming – short & long fibre
  Pipe bending
Short Fibre-PAEK moulded door assembly
Short fibre PAEK to Ti 6Al4V mechanical bonding/Tufting
Thermoplastic fibre wound pipes

## Slide 9: FUTURE ASSEMBLY BONDED JOINTS
Paste adhesive and flexible preform geometry
  OML Control
  Fastener-less Assembly
  Less tooling required
  Thinner Skins
  Simpler detail part geometry
CHALLENGES:
  Wet Assembly – messy!
  Through laminate bondline and cleat assessment
  Noisy materials
BUT WHAT ABOUT THE KISSING BOND!
Low temp cured paste adhesive Pi preform/cleat stiffener/rib

## Slide 10: FUTURE ASSEMBLY KISSING BOND

## Slide 11: NDT CHALLENGES Modern Materials & Assembly Methods
QUESTIONS?
&
THANK YOU