## Slide 1
ET Syllabus & Learning Outcomes
Howard Garlick – Technical & Certification Engineer
howard.garlick@bindt.org +44 (0) 74 8444 8564

## Slide 2
Establishing the foundations
Why do we need a syllabus?
Sets
expectations
Structures
the course
Helps you
plan ahead
Creates
accountability

## Slide 3
Technical Specification 25107:2019
TS 25107:2019 was produced with the aim to harmonize training globally
TS 2517:2019 includes the NDT method of
This basic framework maintains the quality and competence of NDT personnel
Helps ensure trainees are adequately prepared for certification examinations
TS 25107:2019 was adopted by BINDT as a basic framework
Where the syllabus originates
AT
ET
PT
RT
UT
VT
LT
MT
ST
TT

## Slide 4
TS 25107:2019 lacks detail
What do Levels 1, 2 and 3 candidates need to actually know?
Where the gap exists
What frequency is
?
Frequencies used in ET
High frequencies
Low frequencies
Mixing frequencies
Units
Affects on field width
Affects on depth of penetration
Affects on inductive reactance
Affects on capacitive reactance
Affects on impedance
Affects on the impedance plane

## Slide 5
Changing the focus
BINDT is embarking on the introduction of learning outcomes to fill this gap
Example from the initial ET general theory draft courtesy of James Watson
Learning outcomes

## Slide 6
Describe how a magnetic field will penetrate any material but how far it penetrates and what it does during its interaction depends on both the material (predominantly permeability and conductivity) and magnetic field properties (frequency, strength and its distribution).
Frequency
Learning outcomes
Define frequency as the cycles per second, or change per second, that occurs to a quantity such as current, voltage or magnetic flux density. Symbol f, SI unit Hertz (Hz).
Describe a DC current and/or a static magnetic field as having a frequency of zero.
Describe the difference between the frequency related to the change in current/voltage/magnetic field and that of a filter being the removal of frequency components from the signal.
Describe the current in an AC circuit as charge (electrons) moving forwards and backwards at a set frequency.
Describe how current sources are challenging to operate when a large driving power is required, i.e. when there is significant inductive reactance due to: a coil of large inductance and/or high operating frequency.
Describe the increase in strength of electric field / eddy currents formed based on a greater rate of change of magnetic field; including in terms of an increased frequency, stronger applied magnetic field or greater electromagnetic coupling (i.e. reduced lift-off or increased fill factor).
Describe how a lower conductivity material will require a higher frequency to achieve the same sensitivity and separation between lift-off and defect response, compared to that of a higher conductive material.
Describe how a lower frequency may be required for inspecting very conductive materials due to being too sensitive to scratches and other discontinuities that are not of interest.
Describe how testing materials above the Curie point requires additional factors to consider, including the protection of inspection equipment from extreme temperature as well as an assessment of optimum frequency based on a significant reduction in permeability and an increase in material resistivity.
Use Formula 6 to calculate the inductive reactance of an unloaded coil given the frequency and coil inductance values in units that do not need to be converted.
Use the given equation to calculate the inductive reactance of an unloaded coil given the frequency and coil inductance values in units that mayt need to be converted, e.g. kHz to Hz, μH to H.
Describe that there are capacitive effects which can occur if operating a probe at an inappropriate frequency and/or probe cables are too long.
Use Formula 7 to calculate the resonant frequency of a probe given the coil inductance and capacitance in values that may need to be converted, e.g. microhenries to Henries, and/or in standard index form.
Use Formula 6 and Formula 8 to calculate the impedance of a component or circuit given the resistance, frequency and inductance values in units that may need to be converted, e.g. kHz or MHz to Hz, μH to H.
Describe how an increase in frequency increases the impedance of a probe based on an increase in inductive reactance; and vice versa.
Describe how an increase in frequency increases the electrical phase angle via an increase in inductive reactance; and vice versa.
Use Formula 11 to calculate the standard depth of penetration given the resistivity, frequency and relative magnetic permeability in units that do not need to be converted.
Use Formula 11 and rearrange to calculate the frequency required to achieve a required standard depth of penetration, with given resistivity and relative magnetic permeability in units that do not need to be converted.
Use Formula 12 and rearrange as necessary to calculate the standard depth of penetration, material conductivity (or resistivity), relative magnetic permeability or frequency; with given values in units which may or may not require converting.
Describe how a lower frequency should be used on materials with a rough surface to improve signal to noise ratio, as more eddy current is below the surface not affected by these lift-off variations.
Syllabus:
1 reference
Learning outcomes:
35 references

## Slide 7
Continuous improvement
Perceived outcomes:
The benefits
Transparent
Training
Consistency
Candidate
Preparedness
Candidate
Satisfaction
Examination
Results
Examination
Harmonisation
Measurable
Outcomes
Targeted
Pre-Course
Study
Fair

## Slide 8
Future plans
What comes next?
ET Specific
Implementation
Expansion to other methods
Feed into
NAS 410 EN 4179
Feed back into TS 25107
Feed into ISO 9712

## Slide 9
ET user group and working group
Framework is being established
Weldment requirements captured in draft documents
Inclusion of wrought products and corrosion mapping?
One AQB making preparations
Additional work needed on supporting documents
PCN Aero requirements?
ECA developments

## Slide 10
ET Syllabus & Learning Outcomes
Howard Garlick – Technical & Certification Engineer
howard.garlick@bindt.org +44 (0) 74 8444 8564