## Slide 1
Risk Based Part Qualification and the implications for NDT
BINDT – NDT for Metallic Airframe Components
Dr. Simon Lewis
20th April 2021

## Slide 2: About Norton-Straw
Our Team
  A growing team of 20 full time employees
  Engineering and technology specialists with out-of-the box capability
Our Locations
  Derby, UK: Headquarters in Historic Darley Abbey Mills
  Bristol, UK: Historic-quarter of city centre
  Hubs for UK aerospace industry
  Well connected to Europe by East Midlands and Bristol Airport
Our Infrastructure
  We maintain our own high-performance computing capability capable of tackling complex engineering problems without dragging on our customer’s infrastructure
  We hold our own licenses for a suite of industry recognised analysis tools; notably STARCCM+, the ANSYS Workbench suite and ABAQUS

## Slide 3: How to use this document
This is a template document that can be used for:
  Presentations
  Reports issued in the presentation format
  Case studies
Be sure to edit the front page and the revision history with the document details
  Issue date must spell out the month (not, for example, 01/12/2021 as ambiguous in US)
  Choose title appropriate for the document. Plainer title page is more conservative
Choose your title layout, choose whether or not to include watermarks
  Consider the customer, the context of the document, where it will be used.
Find-and-replace to make sure the document number in the footer gets replaced everywhere (including the slide master, so new slides get the new footer)
Change the slide layout by right-clicking on it in the left navigation, choose ‘layout’

## Slide 4: The Role of NDT and Analsysis in Certification
2. Inspection:
Screen out defects where analysis fails
1. Analysis:
Justify acceptance of defects where possible
Defect size
Safe Life
Target life
Max allowable defect size

## Slide 5: The Role of NDT and Analysis in Certification
Inspection Effort / Cost
Analysis Effort / Cost
Increasing Certification Life
Push / Pull between inspection and analysis is necessary
Analysis results set desirable inspection requirements
  What are detection size limits?
Practicalities of inspection define analysis targets
  How much conservatism can be accommodated in the analysis?
How do we achieve the desired certified life at minimum cost / effort?

## Slide 6: Certification via Defect Tolerance
Stress Analysis
Identify limiting location
characteristic stress, temperature etc. from FEA
Number of Cycles
Crack length
Life to Fracture
Fracture mechanics calculations
Critical crack size
Life to failure
Initial Crack size, a
Life to failure
Postulate initial crack
Detectable Crack size
Inspection Cost
Analysis defines a critical defect size.
Inspection is used to ensure no defects above this size enter service

## Slide 7: Where this falls down…
This approach has proved challenging in certifying AM (and other powder metallurgy) parts
Volumetric defects are a concern
AM part geometries are often hard to inspect
M. Gorelik International Journal of Fatigue 94 (2017) 168–177
Inspection
cost
AM parts prohibitively expensive to certify for high safety duty

## Slide 8: Existing Deterministic Approach
Analysis assumes the largest defect at the worst location
Output is deterministic – part is either okay or not (Risk is 1 or 0)
This does not reflect reality!
  Many components won’t have problematic sized defects
  Where there are defects, they may be in positions where they will never present an integrity issue.
If we know something about the likelihood of defects occurring, we can use this information:
  More refined estimate of failure risk
  how it evolves over part lifetime
Probabilistic (or risk based) approach to defect tolerance widely used in Aero Engines, and is the subject of wide investigation for AM parts.
Initial defect size
PDFoccurance

## Slide 9: Probabilistic / Risk Based Assessment Route
Initial defect size
Poccurance
Knowledge of defect distribution
Number of Cycles
Crack length
Life to Fracture
Ncycles
Pfailure
Pf =1
Repeat for a range of defect sizes and sample volumes. Whole component risk can then be estimated, e.g. from weakest link model
Fracture mechanics calculations
Stress Analysis
Split part into sample volumes
characteristic stress, temperature etc. from FEA
Stable crack growth
Cycles to failure
Repeat for many defect sizes
Crack length
Operating Cycles
Probability of Failure
Failure risk vs life for sub volume

## Slide 10: Benefits of Risk Based approach
We can use the results to better target inspection
  Focus on areas where the impact on part risk is most significant
  Avoid inspection effort where the payback on risk is low
Analysis can be used to determine the value of various inspection strategies, using POD curves
Initial defect size
Expected number / unit volume
Stress Data
Zoned Risk Plot
Crude inspection
Intensive inspection
Without Inspection
Operating Life / Cycles
Pfailure
Inspection
cost
Failure risk
Increased life

## Slide 11: What does this mean for NDT and Inspection?
A siloed approach to Analysis and inspection will limit the overall benefit
Design of the Analysis and Inspection strategies must be collaborative
Analysis
Critical crack size
Inspection
Inspection plan
Location / Region POD curves
Component risk map
Defect sizes/locations of interest
Update region defect probability curves
Update inspection strategy

## Slide 12: Summary
Risk based defect tolerance is likely to become increasingly critical for part certification, particularly with the growth of AM components
To make full use of the benefits, much closer engagement will be needed between Analysts, Designers and NDT practitioners
Design/Analysis will need to be conducted with the inspection method, POD curves etc. in mind.